## Slide 1
Weighting of pitch
June 29, 2023
S. Scott (CFS), G. J. Kramer (PPPL), A. Lachmann (PPPL/SULI), H. Zhang (PPPL/PFURO)
This file: 20230629_pitch_weight_01.pptx

## Slide 2: What is the issue?
The ASCOT preprocessor (marker_sets.py) constructs an ensemble of marker that is randomly or uniformly
distributed in the variable ‘pitch’ º l = cos (q) where q is the angle between the velocity vector and the local
B-field direction.
So the ‘density function’ of markers as a function of l is just a constant, N(l) = c.
A marker with some l has a velocity parallel to B-field of V|| = Vl = V cos(q).
A marker with some l therefore has a velocity perpendicular to B-field of V^= sqrt(V2 – (Vl)2) = V sqrt (1 - l2).
Assuming for convenience that the B-field is in the x-direction, then the velocity components in the y- and
z-directions would be Vx = V^ sin(b), Vy = V^ cos(b), where b is the ‘gyro’ angle.
‘Weights’ W(l) are assigned to each l. We want to compute the proper weight function so that
N(l)W(l) represents an isotropic distribution function.
If choosing N(l) = c yields an isotropic distribution function by itself, then W(l) = 1 (i.e. a constant,
not varying with l).

## Slide 3
V
®
q
V|| º V cos q º | V| l
with l º cos q
®
V dq
r = V sin q
this file: 20230628_pitch_weight_02.pptx
Compute velocity space of all velocity vectors having and angle
with respect to the local B-field between q and q + dq
Circumference = 2pr = 2p V sin q
Width of ‘ribbon’ = V dq
So total phase area A is: Circumference x Width
A = (2pV sin q) V dq
= 2pV2 (sin q) dq
= 2pV2 d(cos q)
= 2pV2 d l
--> so the number of alpha particles born with
lo < l < lo + dl is just proportional to dl
and is not a function of l.
Check: total area is = 2pV2 ò d l = 4pV2 ü
-1
1
V|| = Vx
Vy
Vz

## Slide 4
V
®
q1
V dq
r1 = V sin q1
q2
V dq
r2= V sin q2
Compare the cartoon at small q and large q

## Slide 5
But how do we reconcile the weight(l) being unity with the fact that
there are more alphas with q near 90o than with q near 0o?
Consider two ranges of l: l = [0.9,1.0] (i.e. nearly parallel to B) and l = [0., 0.1] (i.e. nearly perp to B)
l = [0.9, 1.0] corresponds to q = [ 25.8, 0] i.e. a range of 25.8o.
l = [0., 0.1] corresponds to q = [90, 84.3] i.e. a range of 5.7o.
Second check: construct an ensemble of markers that is uniformly distributed in l (over[-1,1] ) and
uniformly distributed in pitch angle b (over [0, 2p]). Then compute Vx, Vy, Vz.
Are there the same number of markers with velocity vector near the x-hat direction, the y-hat
direction, and the z-hat direction, i.e. is this constructed ensemble actually isotropic?
Answer: yes
Ans.: same dl covers a bigger dq when
l is near unity, i.e. velocity is nearly
parallel to B

## Slide 6
import pdb
import h5py
import numpy as np
import time as time
import matplotlib.pyplot as plt
import myprompts as MYP
import read_any_file as RAF
import write_a_file as WAF
import matplotlib as mpl
from shapely.geometry import Point, Polygon
from matplotlib.patches import Rectangle
from matplotlib.backends.backend_pdf import PdfPages
import sys
def test_pitch_weight():
Npitch = 3000
Nbeta = 3000
Ntotal = Npitch * Nbeta
vparallel = np.zeros(Ntotal)
vy = np.zeros(Ntotal)
vz = np.zeros(Ntotal)
test_pitch_weight.py
Constructs a marker ensemble uniformly distributed in l
and uniformly distributed in pitch angle (essentially,
at one velocity and one spatial location). Then compute
number of markers with velocity vector nearly in
x-direction, nearly in y-direction, and nearly in z-direction.
If the numbers of markers in these three directions are
nearly the same, then the constructed marker ensemble
is isotrpopic and no special ‘weighting’ of the markers in
l is needed to ensure that the weighted distribution
function isotropic.

## Slide 7
weights = np.zeros(Ntotal)
betas = np.linspace(0., 2.*np.pi, Nbeta, endpoint=False)
pitches = np.linspace(-0.999999, 0.999999, Npitch, endpoint=True)
vtot = 1.3e7 # birth speed of alpha at 3.5 MeV
ictr = 0
for ii in range(Npitch):
for jj in range(Nbeta):
vparallel[ictr] = vtot * pitches[ii]
weights[ictr] = 1
#weights[ictr] = np.sqrt(1 - pitches[ii]**2)
vperp = np.sqrt(vtot**2-vparallel[ictr]**2)
vy[ictr] = vperp * np.cos(betas[jj])
vz[ictr] = vperp * np.sin(betas[jj])
ictr+= 1
weights = weights / np.sum(weights)
ii_parallel = (np.abs(vparallel)/vtot>0.9)
ii_y = (np.abs(vy)/vtot>0.9)
ii_z = (np.abs(vz)/vtot>0.9)
total_weight_parallel = np.sum( weights[ii_parallel])
total_weight_y = np.sum( weights[ii_y])
total_weight_z = np.sum( weights[ii_z])
print(" weight in parallel direction: ", total_weight_parallel)
print(" weight in y direction: ", total_weight_y)
print(" weight in z direction: ", total_weight_z)
sys.exit()
test_pitch_weight.py , continued

## Slide 8
If weights[ictr] = 1:
weight in parallel direction: 0.100000  almost equal weighting in all directions
weight in y direction: 0.099975
weight in z direction: 0.099975
Markers in parallel dirn: 900000  same number of markers in all directions
Markers in y-dir'n: 899776
Markers in z-dir'n: 899776
If weights[ictr] = np.sqrt(1 - pitches[ii]**2)
weight in parallel direction: 0.037215005736784476  too little weight in the parallel direction
weight in y direction: 0.12417961979729016
weight in z direction: 0.12417961979729016
Markers in parallel dirn: 900000
Markers in y-dir'n: 899776
Markers in z-dir'n: 899776